## Slide 1: Personal Networks Application Support Systems
Dr. Martin Jacobsson
Prof.dr.ir. Ignas Niemegeers
Prof.dr.ir. Sonia Heemstra de Groot
Delft University of Technology

## Slide 2: Three Layer View (1)
2
Interconnecting
Structures
P-PAN
Network Level
Service Level
Public service
Private service
Personal node
Foreign node
Cluster
Cluster
Connectivity Level
Interconnecting
Structures
RCD1
RCD2
RCD3
RCD4
RCD5
RCD7
RCD6
PN
Air IF 1
Air IF 2
Air IF 3
Dual Air IF
Radio Controller

## Slide 3: Application Support Systems
Service-Oriented Architectures (SOA)
  Offers self-configuration at the service/application level
  Service discovery
  Service session management
  Access control for PN-PN and Federations
Context Management Framework
  Collect, process, store, distribute context information
Naming
  Naming of devices, services, etc.

## Slide 4
Personal Networks
Application Support Systems
4
    General Concepts
    Service Oriented Architecture
    Context Information Management
    Naming

## Slide 5: Devices, Nodes, and Services
From Freeband PNP2008 (Rieks Joosten)

## Slide 6: Device Sharing
PNs are strongly based on the owner concept
  A single person owns a device!
Sharing and borrowing will be a requirement:
  Families share devices in the house, car, etc
  Friends borrow each other's devices
  Employees borrow company equipment for trips, etc.
  ...
Renting will also be a requirement:
  Car with electronic equipments, ...

## Slide 7: Private vs. Professional Life
A working person does not want two separate PNs:
  One private PN
  One or more professional PNs
He/she wants:
  Only one agenda, email account, etc
  Manage private activities from office
  Distance working from home

## Slide 8: Sharing of a Device
Legenda
Service in a ‘Brown’ session
Service in a ‘Green’ session
From Freeband PNP2008 (Rieks Joosten)

## Slide 9: Distribution of PN Services on Devices
Green visits Brown
PN Services at work
Public PN Services
Green’s
in-car Services
Green’s in-home services
Device and Sensor Mote
Device sharing 2 PNs
Brown’s
in-car Services
Green’s PN
Brown’s PN
From Freeband PNP2008 (Rieks Joosten)
Legenda
Service in a ‘Brown’ session
Service in a ‘Green’ session

## Slide 10: Three Ways to Share Service
Offer a Service from your PN
  Export the service with PN-to-PN or PN Federation mechanisms
Create a new PN that offers the Service
  Export the service with PN-to-PN or PN Federation mechanisms
Allow multiple persons to personalize a device
  Multiple ‘nodes’ on one device
  Multiple instances of the PN networking / application support systems
Networking will be different

## Slide 11
Personal Networks
Application Support Systems
11
    General Concepts
    Service Oriented Architecture
    Context Information Management
    Naming

## Slide 12: Why Service Oriented?
Self-organization also at the service level
  Allows for service discovery
  Choose and combine services
  Hand over between services possible
Offer/user services to/from outside the PN
  Standardized invocation / discovery / mgmt
  Access control

## Slide 13: Service Discovery Domains/Tiers

## Slide 14: Service Management Node (1)

## Slide 15: Service Management Node (2)
MAGNET Service Management Platform (MSMP)
Service
Discovery
Module
INS
Interaction
Module
Service Discovery Adaptation sub-Layer
Service
Ranker
SCMF
Client
Modified UPnP
Device Module
Modified UPnP
Control Point Module
P2P
Service
Overlay
(INS/Twine)
INS
Name
Resolver
(INR)
INR
Name-tree
Service
Repository
UPnP Interface
(SSDP, SOAP, GENA)
Security
Management
AAA
Module
Police
&
Profile
DB
PN-F Service Discovery via the PN Agent
To the SCMF
Service Session Management Module
From IST MAGNET project (Marc Girod Genet, Majid Ghader, et al.)

## Slide 16: Intentional Naming System (INS)
Intentional Naming System (INS)
  Proposed by MIT
  Naming, resource discovery, service location
  For dynamic and mobile networks of devices.
  Applications describe what they are looking for (their intent),
INS/Twine
  Optimization of INS

## Slide 17: Universal Plug and Play (UPnP)
Open standard, Microsoft initiative
Used in DLNA (Digital Living Network Alliance)
Builds on SOAP (http) and XML
Simple Service Discovery Protocol (SSDP)
  Multicasted advertisements / service requests
  Services described with XML
General Event Notification Architecture (GENA)
  Subscribe to events

## Slide 18: TU Delft Implementation
Based entirely on UPnP
Rely on PN-wide broadcasting
Modified gupnp/gssdp (to work with IPv6)

## Slide 19
Personal Networks
Application Support Systems
19
    General Concepts
    Service Oriented Architecture
    Context Information Management
    Naming

## Slide 20: Context Information and Management
Definition of context information (Dey and Abowd)
  “Context is any information that can be used to characterize the situation of an entity”
Provides easy access to dynamic and distributed information
  Relieving application and service developers from dealing with these aspects
  Enables efficient access to frequent requested information
Sharing of information between devices
  Devices may use information otherwise not available to them
  Simple devices may obtain complex and inferred data from high-end devices

## Slide 21: What Does a PN Use Context for?
Networking
  Mobility of user may influence networking
Service discovery
  To locate relevant service(s) to the user
Applications
  Location used to indicate when the user is close to a specific device
  Store user preferences / profiles
PN federation
  Triggering of PN-Federation; context of a user may trigger the need of a PN federation

## Slide 22: Context Management Framework
Data Tier
Middleware Tier
Application Tier
From IST MAGNET project (Rasmus L. Olsen, Martin Bauer, et al.)

## Slide 23: Context Agent
Context Management Interface (CMI)
Processing
&
Storage (P&S)
DSA Manager
Data Source Abstraction
Layer
Information
(to other nodes
and gateways)
Context Access
Manager (CAM)
Context Aware Security Manager
(CASM)
Context Agent
Retriever
Retriever
Retriever
Retriever
Communi-
cation
Module
Context
Agent
Controller (CAC)
Management
(to other nodes
and PN Agent)
From IST MAGNET project (Rasmus L. Olsen, Martin Bauer, et al.)

## Slide 24: Context Modeling
Common, ontology-based context model, modeling entities
XML-based with
  Accuracy
  Confidence
  Etc.
Context Access Language
  synchronous query
  asynchronous subscribe/notify
  modifications
From IST MAGNET project (Rasmus L. Olsen, Martin Bauer, et al.)

## Slide 25: Context Management Architecture
Cluster View
Interconnecting
Infrastructures
PN View
BCN
Basic Context Node
ECN
Enhanced Context Node
CMN
Context Management Node
CMN
BCN
BCN
ECN
ECN
From IST MAGNET project (Rasmus L. Olsen, Martin Bauer, et al.)

## Slide 26
Personal Networks
Application Support Systems
26
    General Concepts
    Service Oriented Architecture
    Context Information Management
    Naming

## Slide 27: Naming
Requirements
  User-friendly names of devices, services, other PNs
  Local namespaces
  Work in PNs (ad hoc networks + tunnels)
mDNS (IETF)
  Multicast discovery of names
  Can be limited to within the PN
MyNet / UIA (Nokia + MIT project)
  Namespaces
  E.g., Printer.Mom.Peter
Intentional Naming System (INS)

## Slide 28: Recap – Application Support
What is the purpose of using a service oriented architecture approach in PNs?
How can a family share a printer and a TV?
What are the differences/similarities between:
  Service discovery
  Context discovery
  Name resolving?