## Slide 1: Personal Network Architecture
Dr. Martin Jacobsson
Prof.dr.ir. Ignas Niemegeers
Prof.dr.ir. Sonia Heemstra de Groot
Delft University of Technology

## Slide 2: Requirements
Easy cross-device applications support based on service oriented architectures (SOA)
Context-awareness
Secure Personal Communication
Automatic Addressing and Network Configuration
Routing, Broadcasting and Mobility
Wireless Technology and Operating System Independent

## Slide 3: Core Concept
Distinguish between:
Personal Nodes
  Devices owned/used/controlled by you
Foreign Nodes
  All other devices
One single and simple security system independent of link layer technologies
  Compare this with Bluetooth, Wifi, VPN, etc.
Personal Network
= The set of all your Personal Nodes

## Slide 4: Three Layer View (1)
Interconnecting
Structures
P-PAN
Network Level
Service Level
Public service
Private service
Personal node
Foreign node
Cluster
Cluster
Connectivity Level
Interconnecting
Structures
RCD1
RCD2
RCD3
RCD4
RCD5
RCD7
RCD6
PN
Air IF 1
Air IF 2
Air IF 3
Dual Air IF
Radio Controller

## Slide 5: Three Layer View (2)
Connectivity Level
  Works on top of available link layers
  Network Level - Intra-cluster
  How are Clusters formed?
  How is the identification of gateways/border nodes done?
Network Level
  Routing and addressing
  Establishment of tunnels and their dynamic maintenance
  How are nodes included in a PN? How to exclude nodes?
  Naming within the PN
Service Level
  Service Discovery
  Context Discovery and Context-aware Service Discovery
  Bridging heterogeneous service platforms

## Slide 6: Personalization of Nodes (1)
Cluster and PN Formation
  A security mechanism is used separate Personal from Foreign Nodes. Clusters contain only Personal Nodes.
  A PN is formed by constructing inter-Cluster tunnels between Personal Clusters.
Personalization
  A new Node is included into the PN (or personalized) by pairing it with a Node already personalized. It becomes a Personal Node.
  An intra-PN security mechanism makes sure that encryption keys are distributed to the new Node and that the PN is aware of the new Node.
  Configuration of the new Node can also take place (such as addressing).

## Slide 7: Personalization of Nodes (2)
Mine
Manual Pairing
Manual Pairing
Implicit Pairing

## Slide 8: Personalization of Nodes (3)
A new Node is included into the PN (or personalized) by pairing it with a Node already personalized.
  It becomes a Personal Node.
An intra-PN security mechanism installs trust relationships between the new Node and the existing Nodes in the PN
  Distribution of encryption keys
Network-related configuration of a Node takes place after personalization
  Such as addressing, awareness of PN Agent

## Slide 9: PN Network Architecture
Personal (Virtual) Network
Cluster
Cluster
Cluster
Cluster
Cl.
Encrypted
Tunnel

## Slide 10: The Big Picture

## Slide 11: When a Node Meets Another Node
A
B
{Hello, A}PID
{Hello, B}PID
{Mgmt Data}PID
{Data}PID

## Slide 12: Personal Networks
Cluster 1
B
A

## Slide 13: Personal Networks
B
A
Cluster 1

## Slide 14: Personal Networks
Office Cluster
P-PAN
Home Cluster
Car Cluster
Infrastructure Networks
Personal Node
Gateway Node
Access Router
Inter-Cluster Tunnels
PN Agent

## Slide 15: Personal Networks
P-PAN
Office Cluster
Home Cluster
Car Cluster
Infrastructure Networks
Personal Node
Gateway Node
Access Router
Inter-Cluster Tunnels
PN Agent

## Slide 16: Personal Networks
P-PAN
Office Cluster
Home Cluster
Car Cluster
Infrastructure Networks
Personal Node
Gateway Node
Access Router
Inter-Cluster Tunnels
PN Agent

## Slide 17: Personal Networks
Office Cluster
Home Cluster
P-PAN
Car Cluster
Infrastructure Networks
Personal Node
Gateway Node
Access Router
Inter-Cluster Tunnels
PN Agent

## Slide 18: Recap - Architecture
Is this device a Personal of Foreign Node?
What is the role of a PN Agent?
If a Personal Node is switched off, is it part of a Personal Network?